## Slide 1
ADSI Inverter Dashboard
Application Overview v2.4.8
Prepared by Engr. Clariden D. Montano, REE

## Slide 2
Project Overview
The ADSI Inverter Dashboard is a SCADA-based monitoring and control platform. It consolidates live telemetry, analytics, ML-driven forecasting, and remote operations into one desktop interface.
Main Highlights:
Real-time inverter and node-level telemetry with supervised control
ML-trained day-ahead forecasting with cap-aware data reconstruction
Solcast integration via free Toolkit - no paid API subscription required
Dynamic per-inverter availability (first non-zero PAC to last zero PAC)
Plant Output Auto Capping for automated generation curtailment
Gateway/Remote architecture with secure replication and standby DB
Cloud backup and restore via OneDrive or Google Drive
Operator messaging, alarm episode tracking, and structured data exports

## Slide 3
Main Dashboard
Central view of real-time plant output, daily generation (TODAY MWh), fleet status chips, PAC output band indicators, and fast inverter start/stop control.

## Slide 4
Plant Output Auto Capping
Automatically regulates total plant output within a defined MW band by sequentially stopping and starting whole inverters. Operators set upper and lower limits, exempt specific units, and preview the control plan before activation. Cap-dispatched actions are scope-tagged in the audit log so the ML forecast engine can reconstruct training data accurately.

## Slide 5
Analytics Dashboard
Interval energy charts with day-ahead forecast overlay, actual vs forecast variance, peak interval tracking, selected date summary metrics, and integrated 7-day weather outlook.

## Slide 6
Energy Generation Tracker
Server-computed current-day energy derived from PAC-based 5-minute intervals. Per-inverter KPI tiles with daily energy totals and single-date energy summary export.

## Slide 7
Daily Performance Report
Per-inverter daily report with energy (MWh), peak/avg PAC, uptime, alarm count, dynamic availability (calculated from each inverter actual production window, not a fixed solar window), and performance ratio. Plant availability averages across all configured inverters including inactive ones.

## Slide 8
Alarms and Alerts
Episode-based alarm tracking with severity, duration, and acknowledgement state. Alarm sound triggers only for sustained unacknowledged episodes exceeding 5 seconds. Same-node alarm value changes within an active episode do not retrigger sound.

## Slide 9
Operations History
Full traceability of all inverter start/stop commands with operator identity, timestamps, and scope tagging. Plant-cap dispatch actions carry scope plant-cap so the forecast training engine can distinguish automated curtailment from manual stops.

## Slide 10
DAY-AHEAD FORECASTING AND SOLCAST

## Slide 11
DAY-AHEAD FORECASTING AND SOLCAST
ML-trained day-ahead forecasting with cap-aware data reconstruction, intraday adjustment, and error memory correction.
Solcast Integration - No Paid Subscription Required: The dashboard uses the free Solcast Toolkit embedded chart for solar forecast visualization. The Toolkit URL is constructed server-side from just three operator inputs: Plant Resource ID, Forecast Days (1-7), and Resolution (PT5M to PT60M).
No Solcast API key or paid subscription is needed. The Toolkit is a publicly available visualization tool provided by Solcast at no cost. This eliminates recurring subscription fees while still providing professional-grade solar irradiance forecast data for day-ahead scheduling and intra-day updates.

## Slide 12
Data Export
Structured Excel and CSV exports for energy summaries, daily reports, trained day-ahead vs actual, Solcast day-ahead vs actual, and Solcast toolkit data. Configurable export paths with separate forecast subfolder routing by source.

## Slide 13
Settings Section
Centralized configuration for plant setup, data retention, polling intervals, plant output cap defaults, Solcast toolkit parameters, gateway/remote connectivity, license management, and auto-updates.
Main Highlights:
Cloud Backup (OneDrive / Google Drive)
Gateway-Remote architecture with WebSocket live bridge
Inverter IP Address and Topology Configuration
Solcast Toolkit Settings (Resource ID, Days, Resolution)
App Updates with auto-download installer

## Slide 14
Data Cloud Backup
Scheduled cloud backup to OneDrive or Google Drive with configurable retention. Supports manual backup, restore with settings preservation, and encrypted credential storage.

## Slide 15
Gateway-Remote Data Synchronization
Gateway-to-remote architecture with incremental cursor-based replication, standby DB refresh (pull), and data push. Remote mode displays live gateway data without local persistence. Operator name is preserved during sync. Manual pull detects local-newer data to prevent accidental overwrites.

## Slide 16
Inverter IP Address Configuration
Configures inverter IP addresses, active node assignments, and polling parameters. Changes apply after confirmation and are protected from accidental remote overwrite during replication.

## Slide 17
Inverter Network Overview
Visual topology map of inverter connectivity, status, and block structure. Quickly identifies online, offline, and degraded devices across the plant network with time-limited auth gate access.

## Slide 18
Application Updates and Version Management
Centralized update interface with auto-check, download, and Restart and Install workflow. Uses coordinated shutdown with soft-stop signaling to Python services before installer handoff.

## Slide 19
Others
Plant Output Auto Capping – automatically curtails generation during negative market price or grid dispatch orders.
Active Alarm Sound – sustained alarm episodes trigger audible alerts to capture operator attention (5-second threshold).
Built-in ML Forecast Engine – trained day-ahead model with cap-aware reconstruction, intraday adjustment, and error memory.
Solcast Toolkit – free embedded forecast visualization using only a Plant Resource ID. No Solcast API subscription or key required.
Downloadable User Guide – comprehensive in-app HTML guide with PDF download covering all 21 sections.
Operator Messaging – compact gateway-to-remote note channel with read receipts and rate limiting.